## Slide 1
END-SEMESTER PRESENTATION
Optimal Configuration of Bifacial Photovoltaic Modules Using Parametric Analysis
B.Tech. Project | Department of Electrical Engineering
Ashish Upadhyay (2022UEE4521) • Pratyai Chakrabarty (2022UEE4586) Aman (2022UEE4532) • Aditya Garg (2022UEE4503)
Supervisor: Dr. Astitva Kumar, Assistant Professor
Netaji Subhas University of Technology (NSUT), New Delhi | May 2026

## Slide 2
Presentation Outline
01 Introduction & Motivation
02 Literature Survey
03 Research Gaps
04 Problem Statement & Objectives
05 Mathematical Formulation
06 Simulink Model & Platform Architecture
07 Case Study: Greater Noida
08 Results & Parametric Analysis
09 Validation with Literature
10 Conclusion & Future Scope
11 Publication & References
[Insert Bifacial PV Diagram / Photo]

## Slide 3
Introduction & Motivation
• Solar PV: fastest-growing electricity source globally — 1,500+ GW installed by 2024 (IEA)
• India targets 500 GW non-fossil capacity by 2030; receives ~5,000 TWh solar energy/year
• Bifacial PV modules capture irradiance on both surfaces → 5–30% higher yield vs monofacial
• First commercial bifacial panels: 1984 — projected to capture ~35% of global PV market by 2027
• Rear-side performance depends critically on tilt angle, ground albedo, and mounting height
• Improper parameter selection negates bifacial advantages → need for optimization frameworks
• Gap: No accessible, location-specific tool exists for combined parametric optimization

## Slide 4
Literature Survey
Guerrero-Lemus et al. [7]: Comprehensive bifacial PV technology review; standardization needs identified
Yusufoglu et al. [2]: Annual energy yield analysis; up to 30% gain at 2m height; log-height dependence
Dincer & Ozer [3]: Parametric analysis of albedo, tilt, height, mounting; 21.2% rear gain for aluminum
Sun et al. [10]: Global perspective; combined tilt-albedo-latitude optimization across locations
Ganesan et al. [4]: n-type PERT bifacial under 5 albedo surfaces; 21.4% avg gain with aluminum
Pelaez et al. [5]: Comparison of 5 irradiance models; ~20% bifacial gain validated against field data
Basak et al. [11]: Tilt optimization specific to bifacial; optimal tilt differs from monofacial

## Slide 5
Research Gaps Identified
1. Limited Combined Analysis — Studies evaluate tilt, albedo, height independently; combined interaction effects largely unexplored
2. Location-Specific Gap — Most studies limited to European/American climates; India-specific validation scarce
3. Accessibility Barrier — Optimization tools require PVsyst, SAM, or MATLAB licenses; inaccessible to many designers
4. Single Optimization Objective — Few frameworks consider dual objectives: max total energy vs. max rear-side gain
5. No Integrated Platform — No web-based tool combines real-time API data retrieval with parametric sweep analysis

## Slide 6
Problem Statement & Objectives
“How can the rear-side energy contribution and overall performance of bifacial PV systems be maximized by optimally selecting tilt angle, ground albedo, and mounting height for a given geographical location?”
Research Objectives
• Develop mathematical model for bifacial PV (front + rear irradiance with view factors)
• Implement in MATLAB/Simulink for I-V and P-V characteristic simulation
• Build web-based frontend platform with NASA POWER API integration
• Perform parametric sweep to identify optimal configurations
• Validate framework through case study and literature comparison

## Slide 7
Mathematical Formulation — Front Irradiance
Eq. (1): G_tot = G_front + G_rear Total effective irradiance on bifacial module
Eq. (2): beam_tilted = DNI × max(0, cos θᵢ) Direct beam on tilted surface
Eq. (3): sky_vf = (1 + cos β) / 2 Sky view factor (Liu-Jordan model)
Eq. (4): gnd_vf = (1 − cos β) / 2 Ground view factor
Eq. (5): G_front = beam + DHI·sky_vf + GHI·ρ·gnd_vf Front irradiance: beam + diffuse + reflected

## Slide 8
Mathematical Formulation — Rear Irradiance & Shadow
Eq. (6): γ_prof = arctan(tan α_sun / cos(γ_sun − γ_panel)) Solar profile angle
Eq. (7): shadow_lower = h / tan(γ_prof) Lower shadow boundary
Eq. (8): shadow_upper = (h+W·sinβ) / tan(γ_prof) Upper shadow boundary
Eq. (9): F_V = ∫ cosθ₁·cosθ₂ / (2r) dx Shadow view factor (Simpson’s rule)
Eq. (10): G_r0 = ρ·DHI·rear_vf + ρ·(GHI−DHI)·(rear_vf−F_V) Rear irradiance with shadow correction
Eq. (11): G_rear = G_r0 × φ_bifaciality Scaled by bifaciality factor (0.7)

## Slide 9
Simulink Model & Implementation
[Insert Simulink Model Screenshot]
• calculate_irradiance MATLAB function implements Equations (1)–(11)
• PV Array block: single-diode model 550 Wp bifacial module, 72×2 half-cells
• V_ramp sweep: 0V → Voc for complete I-V / P-V characteristic curves
• NOCT thermal model for cell temperature derating
• Simpson’s rule numerical integration for shadow view factor F_V (N=200)

## Slide 10
Frontend Platform Architecture
▶ User Interface: City, date range, sweep parameters, albedo surface type, optimization objective
▶ Backend (Node.js): Express server, API routing, input validation, parametric sweep coordination
▶ NASA POWER API: Hourly GHI, DHI, DNI, temperature — any global location, 0.5° resolution
▶ Analysis Engine: Erbs decomposition, Liu-Jordan transposition, view factor computation, I-V/P-V curves
▶ Results Dashboard: Optimal config tables, charts, individual parameter variation analysis

## Slide 11
Case Study: Greater Noida, India
• Location: 28.47°N, 77.50°E
• Date: 13 March 2026
• Height: 50–450 cm (step 50, 9 levels)
• Tilt: 10°–50° (step 10°, 5 levels)
• Albedo: 0.3 (Concrete surface)
• Azimuth: 180° (South-facing)
• Bifaciality factor: 0.7
• Total GHI observed: 6.08 kWh/m²
• Peak GHI: 866.53 W/m²
• 45 evaluation points (9 × 5)
[Insert Frontend Screenshot]

## Slide 12
Results: Maximum Energy Configuration
Optimization Objective: Maximize Total Energy Output
Rank | Height (cm) | Tilt (°) | Surface | Energy (kWh) | Rear Gain (%)
1 | 450 | 30 | Concrete | 3.16843 | 16.55
2 | 450 | 40 | Concrete | 3.16570 | 15.61
3 | 400 | 30 | Concrete | 3.16521 | 16.39
4 | 400 | 40 | Concrete | 3.16258 | 15.45
5 | 350 | 30 | Concrete | 3.16113 | 16.19
✔ Optimal: 30° tilt, 450cm height → closely matches site latitude (28.47°N)
✔ Top 5 differ by < 0.25% in energy → robust performance near optimum
✔ 16.55% rear gain demonstrates significant bifacial advantage over monofacial

## Slide 13
Results: Maximum Rear Gain Configuration
Optimization Objective: Maximize Rear-Side Contribution
Rank | Height (cm) | Tilt (°) | Surface | Energy (kWh) | Rear Gain (%)
1 | 450 | 10 | Concrete | 2.99422 | 17.90
2 | 400 | 10 | Concrete | 2.99130 | 17.76
3 | 350 | 10 | Concrete | 2.98755 | 17.57
4 | 300 | 10 | Concrete | 2.98258 | 17.33
5 | 450 | 20 | Concrete | 3.11109 | 17.33
✔ Max rear gain (17.90%) at 10° tilt — low tilt maximizes ground view factor
✔ Trade-off: 5.5% lower total energy compared to max-energy configuration
✔ Dual optimization enables informed decision-making for system designers

## Slide 14
I-V and P-V Characteristics
[Insert I-V Curve Plot]
[Insert P-V Curve Plot]
• Higher effective irradiance → higher Isc and peak power on I-V curve • MPP shifts with installation configuration changes • Voc relatively stable (logarithmic irradiance dependence)

## Slide 15
Individual Parameter Variation Analysis
Albedo Effect
Fixed: tilt=20°, h=100cm • Aluminum (0.85): 24.72% • Concrete (0.30): ~12% • Asphalt (0.12): < 5% • Near-linear relationship • Most influential parameter • ~5× variation across surfaces
Height Effect
Fixed: tilt=20°, albedo=0.18 • Gain increases with height • 6.61% at h=100cm • Logarithmic dependence • 200-300cm sweet spot • Diminishing returns above • Consistent with [2]
Tilt Effect
Fixed: h=100cm, albedo=0.18 • Max rear gain 7.24% at 10° • Decreases with higher tilt • Front vs rear trade-off • Combined optimization needed for best results • Consistent with [3]

## Slide 16
Validation: Comparison with Literature
Study | Scenario | Reported | This Study
Dincer & Ozer [3] | Aluminum, tilt 20° | 21.2% | 24.72%
Dincer & Ozer [3] | Height 40-100cm | 4.1-4.5% | 5.2-6.6%
Yusufoglu et al. [2] | Albedo=0.2, 2m, Cairo | ~13.8% | 16.55%
Ganesan et al. [4] | Aluminum surface | 21.4% | 24.72%
Pelaez et al. [5] | High albedo config | ~20% | 17.9-24.7%
✔ Consistent trends and magnitudes validate the proposed framework
✔ Slight differences due to geographic location, irradiance conditions, modeling specifics
✔ Albedo sensitivity, height dependency, and tilt optimization all show good agreement

## Slide 17
Conclusion & Key Findings
✔ Comprehensive bifacial PV optimization framework developed with validated math model (Eqs. 1–11)
✔ Optimal for Greater Noida: 30° tilt, 450cm height → 16.55% rear gain, 3.168 kWh
✔ Albedo is dominant parameter: ~5× variation in rear gain across surface types
✔ Height shows logarithmic benefit; 200–300cm is the practical sweet spot
✔ Dual optimization reveals quantifiable trade-off: max energy vs max rear gain
✔ Web platform makes bifacial optimization accessible without commercial software
✔ Results validated against Dincer & Ozer, Yusufoglu et al., Ganesan et al., Pelaez et al.

## Slide 18
Future Scope
1. Annual energy yield simulation (365-day aggregated analysis)
2. Multi-row array modeling with inter-row shading effects
3. Machine learning-based rapid optimization (surrogate models)
4. Techno-economic analysis with LCOE integration
5. Real-time IoT monitoring & adaptive optimization
6. GIS integration for regional deployment planning
7. Single/dual-axis tracking system comparison
8. Anisotropic sky models (Perez / Hay-Davies)

## Slide 19
References
[1] B.Y.H. Liu, R.C. Jordan, Solar Energy, vol. 4, 1960
[2] U.A. Yusufoglu et al., IEEE J. Photovolt., vol. 5, 2015
[3] F. Dincer, E. Ozer, Energies, vol. 18, 2025
[4] K. Ganesan et al., Solar Energy, vol. 252, 2023
[5] S.A. Pelaez et al., IEEE J. Photovolt., vol. 9, 2019
[6] N. Riedel-Lyngskjaer et al., Solar Energy, vol. 231, 2022
[7] R. Guerrero-Lemus et al., RSER, vol. 60, 2016
[8] M. Alam et al., SETA, vol. 57, 2023
[9] C. Deline et al., NREL Tech. Rep., 2019
[10] X. Sun et al., Appl. Energy, vol. 212, 2018
[11] A. Basak et al., Appl. Energy, vol. 345, 2025
[12] U. Peter, M. Novak, J. Sustain. Energy Syst., 2025
[13] M.H. Aksoy, H.A. Ceylan, RERJ, vol. 13, 2023
[14] N. Baghel et al., Solar Energy, vol. 250, 2023
[15] I.N. Atalay et al., Solar Energy, vol. 246, 2023
[16] D.S. Braga et al., REES, vol. 8, 2023
[17] A.F. Almarshoud et al., Energies, vol. 17, 2024
[18] M.T. Patel et al., IEEE J. Photovolt., vol. 11, 2021
[19] J.A. Duffie, W.A. Beckman, Wiley, 2013
[20] B. Marion et al., IEEE PVSC, 2017
[21] P.K. Sahu et al., Solar Energy, vol. 262, 2023
[22] C. Ghenai et al., Solar Energy, vol. 223, 2021

## Slide 20
Thank You!
Questions & Discussion
Publication: "Performance Analysis of Bifacial PV System Based on Different Albedos" Accepted at IC2PCT 2026 (International Conference on Clean and Prospective Computing Technologies)
Supervisor: Dr. Astitva Kumar | Dept. of Electrical Engineering, NSUT, New Delhi