## Slide 1
END-SEMESTER PRESENTATION
Optimal Configuration of Bifacial Photovoltaic Modules Using Parametric Analysis
B.Tech. Project | Department of Electrical Engineering
Ashish Upadhyay (2022UEE4521) • Pratyai Chakrabarty (2022UEE4586) Aman (2022UEE4532) • Aditya Garg (2022UEE4503)
Supervisor: Dr. Astitva Kumar, Assistant Professor
Netaji Subhas University of Technology (NSUT), New Delhi | May 2026

## Slide 2
Presentation Outline
01 Introduction & Motivation
02 Literature Survey
03 Research Gaps
04 Problem Statement & Objectives
05 Mathematical Formulation
06 Simulink Model & Platform Architecture
07 Case Study: Greater Noida
08 Results & Parametric Analysis
09 Validation with Literature
10 Conclusion & Future Scope
11 Publication & References
[Insert Bifacial PV Diagram / Photo]

## Slide 3
Introduction & Motivation
• Solar PV: fastest-growing electricity source globally — 1,500+ GW installed by 2024 (IEA)
• India targets 500 GW non-fossil capacity by 2030; receives ~5,000 TWh solar energy/year
• Bifacial PV modules capture irradiance on both surfaces → 5–30% higher yield vs monofacial
• First commercial bifacial panels: 1984 — projected to capture ~35% of global PV market by 2027
• Rear-side performance depends critically on tilt angle, ground albedo, and mounting height
• Improper parameter selection negates bifacial advantages → need for optimization frameworks
• Gap: No accessible, location-specific tool exists for combined parametric optimization

## Slide 4
Literature Survey
Guerrero-Lemus et al. [7]: Comprehensive bifacial PV technology review; standardization needs identified
Yusufoglu et al. [2]: Annual energy yield analysis; up to 30% gain at 2m height; log-height dependence
Dincer & Ozer [3]: Parametric analysis of albedo, tilt, height, mounting; 21.2% rear gain for aluminum
Sun et al. [10]: Global perspective; combined tilt-albedo-latitude optimization across locations
Ganesan et al. [4]: n-type PERT bifacial under 5 albedo surfaces; 21.4% avg gain with aluminum
Pelaez et al. [5]: Comparison of 5 irradiance models; ~20% bifacial gain validated against field data
Basak et al. [11]: Tilt optimization specific to bifacial; optimal tilt differs from monofacial

## Slide 5
Research Gaps Identified
1. Limited Combined Analysis — Studies evaluate tilt, albedo, height independently; combined interaction effects largely unexplored
2. Location-Specific Gap — Most studies limited to European/American climates; India-specific validation scarce
3. Accessibility Barrier — Optimization tools require PVsyst, SAM, or MATLAB licenses; inaccessible to many designers
4. Single Optimization Objective — Few frameworks consider dual objectives: max total energy vs. max rear-side gain
5. No Integrated Platform — No web-based tool combines real-time API data retrieval with parametric sweep analysis

## Slide 6
Problem Statement & Objectives
“How can the rear-side energy contribution and overall performance of bifacial PV systems be maximized by optimally selecting tilt angle, ground albedo, and mounting height for a given geographical location?”
Research Objectives
• Develop mathematical model for bifacial PV (front + rear irradiance with view factors)
• Implement in MATLAB/Simulink for I-V and P-V characteristic simulation
• Build web-based frontend platform with NASA POWER API integration
• Perform parametric sweep to identify optimal configurations
• Validate framework through case study and literature comparison

## Slide 7
Mathematical Formulation — Front Irradiance
Eq. (1): G_tot = G_front + G_rear Total effective irradiance on bifacial module
Eq. (2): beam_tilted = DNI × max(0, cos θᵢ) Direct beam on tilted surface
Eq. (3): sky_vf = (1 + cos β) / 2 Sky view factor (Liu-Jordan model)
Eq. (4): gnd_vf = (1 − cos β) / 2 Ground view factor
Eq. (5): G_front = beam + DHI·sky_vf + GHI·ρ·gnd_vf Front irradiance: beam + diffuse + reflected

## Slide 8
Mathematical Formulation — Rear Irradiance & Shadow
Eq. (6): γ_prof = arctan(tan α_sun / cos(γ_sun − γ_panel)) Solar profile angle
Eq. (7): shadow_lower = h / tan(γ_prof) Lower shadow boundary
Eq. (8): shadow_upper = (h+W·sinβ) / tan(γ_prof) Upper shadow boundary
Eq. (9): F_V = ∫ cosθ₁·cosθ₂ / (2r) dx Shadow view factor (Simpson’s rule)
Eq. (10): G_r0 = ρ·DHI·rear_vf + ρ·(GHI−DHI)·(rear_vf−F_V) Rear irradiance with shadow correction
Eq. (11): G_rear = G_r0 × φ_bifaciality Scaled by bifaciality factor (0.7)

## Slide 9
Simulink Model & Implementation
[Insert Simulink Model Screenshot]
• calculate_irradiance MATLAB function implements Equations (1)–(11)
• PV Array block: single-diode model 550 Wp bifacial module, 72×2 half-cells
• V_ramp sweep: 0V → Voc for complete I-V / P-V characteristic curves
• NOCT thermal model for cell temperature derating
• Simpson’s rule numerical integration for shadow view factor F_V (N=200)

## Slide 10
Frontend Platform Architecture
▶ User Interface: City, date range, sweep parameters, albedo surface type, optimization objective
▶ Backend (Node.js): Express server, API routing, input validation, parametric sweep coordination
▶ NASA POWER API: Hourly GHI, DHI, DNI, temperature — any global location, 0.5° resolution
▶ Analysis Engine: Erbs decomposition, Liu-Jordan transposition, view factor computation, I-V/P-V curves
▶ Results Dashboard: Optimal config tables, charts, individual parameter variation analysis